## Slide 1: TransViz
Unreal Engine 4
Implementation Detials

## Slide 2: Index
Preliminary
Design (TransViz Library)
Design (UE4)
  Mesh Generation
  Materials
  Multiplayer – for collaboration
Usage

## Slide 3: Preliminary
Refer to this – See how TransViz generates OSG Node
\\192.168.0.122\Users\Naman\TransVizKT

## Slide 4: Design (TransViz Library)
TransVizUtilUE
  Main interface used to access TransViz library from UE
ITransVizCallBack
  GeomObj returns TransViz generated geometry structure to App
TransVizGeom
  Structure in which TransViz returns model to UE.
  Comprises of Vertex, Normals Vertex Color, Vertex mode and Material Information
UnrealEngineSPU
  Much like SceneGraphSPU that generates osg node from gl stream, UnrealEgineSPU generates TransVizGeom from gl stream.
Note- Instead of open thread for running TransViz server code. We are using std::thread

## Slide 5: Design (UE)
  Mesh Generation
  TransVizCB
    Receives TransVizGeom from TV library
  TVActor
    The TV server code fires up in actors beginplay() function
    After receiving the TransVizGeom the actor converts it to Procedural Mesh. Procedural Mesh needs triangle indexes. This is computed using vertex mode. While vertex and Normal are passed as they are.
    TransViz connection parameters can be set (see. hostname and port)

## Slide 6: Design (UE)
  Material
  Material information (Ambient, Diffuse, Specular, Emission and Shininess) are sent from TransViz
  This information is then pass to DefaultMaterial as parameters
  GLmode is also sent as a part of Material information. This can be used for transparency.

## Slide 7: Design (UE)
  Collaboration
    The TransViz Server code only runs on the server code of TVActor
    Collaboration is achieved using Unreal’s NetMulticast function
    Procedural mesh parameters are sent over the network with NetMulticast DrawNetProcMesh
    SetReplicates(true); is important to replicate actor at all the UE’s multiplayers node

## Slide 8: Usage
  TransViz library
    Generate TransViz solution with “initTransViz.bat UE”. It build TransViz in VS2017 which is used by UE 4.22
    Build and Install the Project in Release mode. Debug mode doesn’t works with UE.
    Build folder containing the library will be generated
  UE
    Copy the content of Build folder to <UEProject>/ThridParty/ TransVizUE.
    Use TV Replication project. Refer to the TVReplication.Build.cs file for adding a library to a UE project
    Refer to TvActor class for implementation.
    Place TvActor in the map.
    Start the mothership. Run the game, The the GL application and then press Alt + A. Model will be generated in the game.